## Slide 1
RISC-V LOOP UNROLLING STRATEGY SELECTION
Compiler Optimization Using RISC-V and Logisim
1
Presented by 2620030312
2620030316
2620030321
Group=7

## Slide 2
2. INTRODUCTION TO RISC-V
RISC-V is an open-standard Instruction Set Architecture (ISA) based on the RISC design philosophy.
An ISA defines instructions, registers, data types, memory-access rules, and other processor behaviors expected by software.
RISC-V is not a specific processor; it is an instruction-set specification that can be implemented by different processor designs.
OPEN & FREELY IMPLEMENTABLE
LOAD / STORE
GENERAL-PURPOSE REGISTERS
MODULAR EXTENSIONS
RISC-based simple instruction design
Different implementations can have different pipelines, caches, and execution resources.
2

## Slide 3
3. WHAT IS LOOP UNROLLING?
NORMAL LOOP
LOAD data
ADD value
STORE data
INCREMENT counter
BRANCH → REPEAT
4× UNROLLED LOOP
LOAD → ADD → STORE
LOAD → ADD → STORE
LOAD → ADD → STORE
LOAD → ADD → STORE
LOOP CONTROL → BRANCH
KEY IDEA
Replicate the loop body multiple times.
Execute multiple original iterations in one new loop iteration.
Reduce how often loop-control instructions are executed.
4× unrolling performs four original iterations before returning to loop control.
3

## Slide 4
4. UNROLLING FACTOR AND 4× UNROLLING
1× Original
2× 2 copies
4× 4 copies
8× 8 copies
16× 16 copies
4× UNROLLED LOOP
a[i] += 1
a[i+1] += 1
a[i+2] += 1
a[i+3] += 1
i = i + 4
Check condition → Branch
1 branch / 1 element
1 branch / 4 elements
Higher factors reduce loop-control overhead further.
Higher factors also increase code size and resource requirements.
The largest factor is not necessarily the fastest.
4

## Slide 5
5. BENEFITS OF LOOP UNROLLING
1. Reduced loop-control overhead
2. Fewer branch instructions
3. Reduced branch frequency
4. Greater instruction-level parallelism
5. Better pipeline utilization
6. More compiler optimization opportunities
7. Potentially lower execution time
LOAD → ADD → STORE | LOOP CONTROL OCCURS LESS OFTEN
5

## Slide 6
6. DRAWBACKS AND TRADE-OFFS
CODE SIZE ↑
REGISTER PRESSURE ↑
I-CACHE PRESSURE ↑
DIMINISHING RETURNS
Duplicating the loop body creates more instructions and can increase instruction-cache pressure.
More values may need to remain in registers; insufficient registers can cause register spilling.
Larger unrolled loops can occupy more instruction-cache space and increase instruction-fetch delays.
Increasing the unrolling factor does not guarantee proportional performance improvement.
MORE UNROLLING ≠ ALWAYS MORE PERFORMANCE
6

## Slide 7
7. FACTORS AFFECTING UNROLLING STRATEGY
LOOP BODY
Size + complexity
ITERATIONS
Count + remainder
REGISTERS
Availability + spills
I-CACHE
Capacity + behavior
MEMORY MIX
Loads, stores, branches
MICROARCHITECTURE
Pipeline + issue width
GOAL: BALANCE PERFORMANCE GAIN AGAINST RESOURCE COST
7

## Slide 8
8. PERFORMANCE COMPARISON AND STRATEGY SELECTION
Unrolling
Execution Time
Code Size
Overall Result
1×
100
Small
Baseline
2×
85
Moderate
Improved
4×
72
Larger
BEST
8×
75
Very large
Slightly worse
EXECUTION TIME
1×
100
2×
85
4×
72
8×
75
RESULT: 4× IS THE SWEET SPOT IN THIS EXAMPLE
Hypothetical comparison: the best factor depends on the loop and target processor.
8

## Slide 9
9. LOGISIM IMPLEMENTATION
PC
Instruction Memory
Control Unit
Register File
ALU
Data Memory
Write Back
4× UNROLLED LOOP
LOAD a[i] → ADD 1 → STORE
LOAD a[i+1] → ADD 1 → STORE
LOAD a[i+2] → ADD 1 → STORE
LOAD a[i+3] → ADD 1 → STORE
i = i + 4
i < n ? YES → LOOP | NO → END
LOGISIM COMPONENTS
Input Pins
Registers
Adders
Comparator
Multiplexer
RAM / ROM
Clock and Wires
Demonstration: four useful operations are performed before loop-control and branch operations repeat.
9

## Slide 10
10. CONCLUSION
More Unrolling
Less Loop Overhead
More Instruction-Level Parallelism
BUT: Larger Code + More Resource Usage
Possible Performance Loss
RISC-V provides an open-standard ISA for processor design.
Loop unrolling reduces the frequency of loop-control and branch instructions.
Unrolling can improve instruction-level parallelism and potentially reduce execution time.
Excessive unrolling can increase code size, register pressure, and instruction-cache pressure.
The optimal unrolling factor depends on the loop and the processor.
In the given example, 4× provides the best performance-versus-resource balance.
OPTIMAL LOOP UNROLLING IS A BALANCE, NOT A MAXIMUM.
THANK YOU
10